Arcade Asteroids on the Apple IIGS

Asteroids Arcade Machine

- Asteroids hardware is based around a 1.5MHz 6502 that handles game logic and writes commands to a display list in shared memory to render the entire screen every frame.
- The 6502 has no direct access to vector display hardware.
- The display list comprises commands to set the current beam position and vector drawing primitives, but most frequently used are JSR commands into the Digital Vector Generator (DVG) processor ROM.
- The arcade ROM runs on the Apple II with just 2 instructions (4 bytes) patched to NOP!
- I have reverse-engineered and commented the arcade 6502 code (based on and extending the work of Lonnie Howell and Chris Cantrel on computerarcheology.com) and re-created a source file that can be re-assembled to produce an exact binary match with the arcade ROM, or alternatively relocated (along with all hardware addresses) anywhere in memory.

On the Apple II GS

- The Apple IIGS runs at 2.8MHz but video memory access is restricted to 1MHz.
- The 65816 runs in 6502 mode (@ 2.8MHz) to execute one iteration of the main arcade code loop, then switches to native (16-bit) mode to process the display list and render a frame.
- The display list format has been overhauled to eliminate unnecessary processing and replace most legacy DVG processor commands with ‘tokens’ to render different objects.
- The command to set the beam position remains unchanged and the rendering routine instead scales the coordinates and calculates the corresponding Apple IIGS SHR screen address for use by subsequent tokenised DVG commands.
- Rendering routines choose the appropriate bitmap based on the DVG command ‘token’ and command parameters, eg. asteroid size and shape, or ship direction.

Challenges on the Apple IIGS

- 1.5MHz 6502 with no video display tasks vs 1/2.8MHz CPU that must erase & render the entire frame every iteration.
- Slow access to IIGS SHR memory due to 2.8<->1MHz interface.
- IIGS SHR memory is 4BPP so entire display is 32KB to manage.
- 1024x1024 effective resolution reduced to 256x192 on the IIGS.
- Keyboard limitations mandate joystick required, with associated polling delays.

Optimisations on the IIGS

- Display list commands replaced with 2-byte ‘tokens’ for each object to be displayed.
- 64 distinct player ships replaced by just 24.
- Explosions (shrapnel) the same shape/pattern but slightly reduced in size.
- 17KB of ‘compiled sprites’ for erase & render routines to minimise video memory accesses.

T.B.D.

- Player ship explosions
- Precise alignment of objects on IIGS display
- Eliminate flicker
- Throttle the frame rate (currently slightly faster than the arcade!)
- Add sound